Reg. Address	name	bits assigned	Description

32 bit registers

0 (x00)	MARS slow control	32	0 (x00)	soft trigger
1 (x02)	configuration load
2 (x04)	config. fifo reset
3 (x08)	config asic 1
4 (x10)	config asic 2
5 (x20)	config asic 3
6 (x40)	state machine reset
7 (x80)	asic global reset
8 (x100)	v1 fix daq, fix for v1 lockup
9 (x200)	v1 ced rst, fix for v1 lockup

1(x04)	Test data	1 bit	Enable test data of DDR transfer
2(x08)	MARS configuration reg.	32 bit	reg to load 433 bit asic config.
3(x0C)	AXI HP control	16 bit	0(0x00)	AXI reset
1(0x02)	fifo reset
4(x10)	AXI DDR3 burst	1 bit	enable DDR burst
5(x14)	Zed board LEDs	32 bit	8 leds lower order bits
6 (x18)	number of ADC reads	32 bit	adc reads per daq
7 (x1C)	FPGA version	32 bit
8 (x20)	Test pulser enable	1 bit	enable test pulser
9 (x24)	ADC write reg.	not used
10 (x28)	ADC read reg. Address	not used
11 (x2C)	ADC read reg.	not used
12 (x30)	not used
13 (x34)	MARS clock	8 bit	reg to divide MARS clk 2^^N
0(x00)
1(x02)
2(x04)
3(x08)

14(x38)	MARS timing delays	24 bit	DAQ timing delays
15(x3C)	MARS busy flag	1 bit	read register for MARS busy
16(x40)	test pulser “on” delay	32 bit	count down register for rising edge
17(x44)	test pulser “off” delay	32 bit	count down register for falling edge

Table 2a Single channel register map
        LSB	MSB
DPO	DP1	DP2	DP3	NC	DA0	DA1	DA2	SEL	NC	SM	ST

        Table 2b ASIC channels registers map.
Channel Registers
Register Bit Position	Bits	Name	Default Value	Description
1:4+(CH-1) x 12	128	DP0:DP3	0	Pile-up rejector trim DAC.
5+(CH-1) x 12	32	NC	0	No connect
6:8+(CH-1) x 12	96	DA0-DA2	0	Threshold trim DAC, 3.5mV step, 3-bit per channel, 111=0V, 000= ‑24.5mV.
9+(CH-1) x 12	32	SEL	0	Channel monitor select. 0 = leakage monitor, 1 = shaper oputput monitor.
10+(CH-1) x 12	32	NC	0	No connect
11+(CH-1) x 12	32	SM	0	Channel mask, SM = 1 (front-end shut-down).
12+(CH-1) x 12	32	ST	0	Test capacitor 30fF, ST = 1 (enable test capaitor).
	384	Channel Bits

        Table 2c ASIC global registers map.
Global Registers
Register Bit Position	Bits	Name	Default Value	Description
385:394	10	PA0:PA9	0:0	10-bit DAC for threshold, 2V full scale, ~2mV step, 0V baseline. 0:0=baseline.
395:404	10	PB0:PB9	0:0	10-bit DAC for test pulse, 2V full scale, ~2mV step, 0mV baseline, followed by 1:40 voltage divider. 0:0=baseline.
405	1	RM	0	RM = 1, synchronous readout. RM = 0, asynchronous readout.
406	1	SENFL1	0	When high, acquisition is internally disabled when any channel finds a peak.
407	1	SENFL2	0	When high, acquisition is internally disabled when any channel exceeds threshold.
408	1	M0	0	M0=1 channel monitor; M0=0 other monitors. Used with bits C0:C4.
409	1	M1	0	M1 = 0, Peak detector output is on PINS PD/PDN. / M1 = 1, monitors are also available on PINS PD/PDN.
410	1	SBN	0	Enable inverting buffer for peak detector and analog monitor outputs. 0=disabled.
411	1	SB	0	Enable buffer for peak detector and analog monitor outputs. 0=disabled.
412	1	SL	0	Internal leakage current generator (used with bit SLH) 0 = 2 pA, 1= Disabled
413:414	2	T0:T1	0:0	Binary coded selection of shaping time. 00=0.25µs, 10=0.5µs, 01=1µs, 11=2µs.
415	1	RT	0	When high, the duration of the ramp is multiplied by a factor of three.
416	1	SPUR	0	Pile-up rejector enable
417	1	SSE	0	Enables comparator multiple firing suppressor. Suppression time adjusted with SS0:SS1.
418:419	2	TR0:TR1	0:0	For RT = 0: 00 = 1us, 01 = 2us, 10 = 3 us, 11 = 4us / For RT = 1: 00 = 3us, 01 = 6us, 10 = 9 us, 11 = 12us
420:421	2	SS0:SS1	0:0	Adjusts multiple firing suppression time. 00=250ns, 10=500ns, 01=1µs, 11=2µs.
422:426	5	C0:C4	0:0	Selector Address Bits Pin AUX / M0 C0 C1 C2 C3 C4 / 0 0 0 0 x x Monitor OFF / 0 0 0 1 x x Temperature / 0 1 0 1 x x Baseline / 0 0 1 1 x x Threshold / 0 1 1 1 x x Test / 1 x x x x x Channel monitor / Address bits: 00000 = Ch0, 11111 = Ch.31. / M1 = 0, Peak detector output is on PINS PD/PDN. / M1 = 1, monitors are available on PINS PD/PDN.
427:28	2	G0:G1	0	Gain selection: 00=600mV/fC), 01=1200mV/fC, 10=1800mV/fC, 11= 3600 mV/fC.
429	1	SLH	0	0 = leakage current set by bit SL, 1= leakage current multiplied by 4.
430	1	SP	0	Select polarity. 0 = negative charge. 1= positive charge.
431	1	SAUX	0	SAUX = 1, output monitor is on pin AUX, 0 = tristate.
432	1	SBM	0	SBM = 1, enable output monitor buffer, 0 = bypass.
433	1	TM	0	TimingMode TM = 0, time of arrival. TM = 1, time over threshold.
	49	Global Bits